## Slide 1: TCP/IP Computer Networks Networks and Internet Topology
José Legatheaux Martins
Departamento de Informática da
FCT/UNL

## Slide 2: Lecture Overview
Router-level topology with a single network
  Points of Presence (PoPs)
  Backbone and enterprise network topologies
AS-level topology of the Internet
  Autonomous System (AS) numbers
  Tier-1 ISPs, regional providers, and stub ASes
  Business relationships between Ases
Using some slides from the course
  Computer Networks, COS461, Jennifer Rexford, Princeton University, 2007 Edition

## Slide 3: Router-level topology of a network

## Slide 4: Intra-AS Topology
Node: router
Edge: link

## Slide 5: Hub-and-Spoke Topology
Single hub node
  Common in enterprise networks
  Main location and satellite sites
  Simple design and trivial routing
Problems
  Single point of failure
  Bandwidth limitations
  High delay between sites
  Costs to backhaul to hub

## Slide 6: Campus Example
Hub-and-spoke
  Four hub routers and many spokes
Hub routers
  Outside world
  Dorms
  Academic and administrative buildings
  Servers

## Slide 7: Simple Alternatives to Hub-and-Spoke
Dual hub-and-spoke
  Higher reliability
  Higher cost
  Good building block
Levels of hierarchy
  Reduce backhaul cost
  Aggregate the bandwidth
  Shorter site-to-site delay
…

## Slide 8: Traditional Data-Center Routing Levels
CR
CR
AR
AR
AR
AR
. . .
S
S
DC-Layer 3
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
DC-Layer 2
Key
CR = Core Router (L3)
AR = Access Router (L3)
S = Ethernet Switch (L2)
A = Rack of app. servers ≈ 40 servers each
A pod has ≈ 20 to 25 racks
~ 1,000 servers/pod == IP subnet
S
S
S
S
S
S

## Slide 9: Capacity Mismatch
CR
CR
AR
AR
AR
AR
S
S
S
S
A
A
A
…
S
S
A
A
A
…
. . .
S
S
S
S
A
A
A
…
S
S
A
A
A
…
~ 5:1
~ 40:1
~ 200:1

## Slide 10: Rings
Rings are a cost effective alternative
  Less links
  Still redundant
  But, longer site-to-site delay
  Most rings are bidirectional
  Adopted in many MAN
…
…
…
…

## Slide 11: Backbone Networks
Backbone networks
  Multiple Points-of-Presence (PoPs)
  Lots of communication between PoPs
  Accommodate traffic demands and limit delay

## Slide 12: Abilene Internet2 Backbone

## Slide 13: Where to Locate Nodes and Links
Placing Points-of-Presence (PoPs)
  Large population of potential customers
  Other providers or exchange points
  Cost and availability of real-estate
  Mostly in major metropolitan areas
Placing links between PoPs
  Already fiber in the ground
  Needed to limit propagation delay
  Needed to handle the traffic load

## Slide 14: Tier-1 ISP: e.g. Sprint

## Slide 15: POP: Point of Presence
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 16
An European Backbone: Géant

## Slide 17
Connecting Continents

## Slide 18
Several Interconnected Backbones

## Slide 19
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Internet Structure

## Slide 20
No centro da Internet encontramos
  “tier-1” transit ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g, Google)
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
CDN (Google)
IXP
Internet Structure

## Slide 21: AS-level topology of the Internet

## Slide 22: Internet Routing Architecture
Divided into Autonomous Systems
  Distinct regions of administrative control
  Routers/links managed by a single “institution”
  Service provider, company, university, …
“Hierarchy” of Autonomous Systems
  Large, tier-1 provider with a worldwide backbone
  Medium-sized regional provider with smaller backbone
  Small network run by a single company or university
Interaction between Autonomous Systems
  Internal topology is not shared between ASes
  … but, neighboring ASes interact to coordinate routing

## Slide 23: Autonomous System Numbers
AS Numbers are 16 bit values.
Level 3: 1
MIT: 3
Harvard: 11
Yale: 29
Princeton: 88
EUnet: 286 (now KPN)
EUnet Portugal: 1897 (1990 ....)
RCCN Portugal: 1930 (1990 ....)
AT&T: 7018, 6341, 5074, …
UUNET: 701, 702, 284, 12199, …
Sprint: 1239, 1240, 6211, 6242, …
…
Currently just over 40,000 in use.

## Slide 24: AS Topology
Node: Autonomous System
Edge: Two ASes that connect to each other
1
2
3
4
5
6
7

## Slide 25: Types of ASs
Stub AS: it is a pure customer of a provider AS. In fact, it doesn’t need to be a real AS with a specific number
Multihomed AS: it is an AS that has connections to more than than one AS but refuses to carry transit traffic
Transit AS: an AS that has connections to more than one other AS and that is designated to carry both transit and local traffic

## Slide 26: What is an Edge, Really?
Edge in the AS graph
  At least one connection between two ASes
  Some destinations reached from one AS via the other (a transit AS)
AS 1
AS 2
d
Exchange Point
AS 1
AS 2
d
AS 3

## Slide 27: Interdomain Paths
1
2
3
4
5
6
7
Client
Web server
Path: 6, 5, 4, 3, 2, 1

## Slide 28: Business Relationships
Neighboring ASes have business contracts
  How much traffic to carry
  Which destinations to reach
  How much money to pay
Common business relationships
  Customer-provider
    E.g., FCT/UNL is a “customer” of RCCN
    E.g., GEANT is a “provider” of RCCN
  Peer-peer
    E.g., RCCN is a peer of PT Comunicações
    E.g., AT&T is a peer of Sprint

## Slide 29: Customer-Provider Relationship
Customer needs to be reachable from everyone
  Provider tells all neighbors how to reach the customer
Customer does not want to provide transit service
  Customer does not let its providers route through it
d
d
provider
customer
customer
provider
Traffic to the customer
Traffic from the customer
advertisements
traffic

## Slide 30: Advertisements and routing
AS1 knows there is a path to a destination if it received an advertisement from another AS telling it
  E.g. provider tells all neighbors that the customer is reachable through it
ASs only route packets to destinations which existence they learned from advertisements
d
customer
provider
advertisements
traffic

## Slide 31: Customer Connecting to a Provider
Provider
Provider
1 access link
2 access links
Provider
2 access routers
Provider
2 access PoPs

## Slide 32: Multi-Homing: Two or More Providers
Motivations for multi-homing
  Extra reliability, survive single ISP failure
  Financial leverage through competition
  Better performance by selecting better path
  Gaming the 95th-percentile billing model
Provider 1
Provider 2

## Slide 33: Peer-Peer Relationship
Peers exchange traffic between customers
  AS exports only customer routes to a peer
  AS exports a peer’s routes only to its customers
  Often the relationship is settlement-free (i.e., no $$$)
peer
peer
Traffic to/from the peer and its customers
d
advertisements
traffic

## Slide 34: AS Structure: Tier-1 Providers
Tier-1 transit provider
  Has no upstream provider of its own
  Typically has a national or international backbone
  For example, it has a transit only AS
  UUNET, Sprint, AT&T, Level 3, …
Top of the Internet hierarchy of 12-20 ASes
  Full peer-peer connections between tier-1 providers
Tier-1 CDN provider
  Has no or low number of upstream provider of its own
  Typically has an international backbone connecting data centers
  Has many caching server POPs
  Offers peering for free

## Slide 35: Efficient Early-Exit Routing
Diverse peering locations
  Both sides of the Atlantic, both costs of US, middle of US, middle of Europe, …
Comparable capacity at all peering points
  Can handle even load
Consistent routes
  Same destinations advertised at all points
  Same AS path length for a destination at all points
Customer A
Customer B
multiple
peering
points
Provider A
Provider B
Early-exit
routing

## Slide 36: AS Structure: Other ASes
Tier-2 providers
  Provide transit service to downstream customers
  … but, need at least one provider of their own
  Typically have national or regional scope
  E.g., Minnesota Regional Network, RCCN, ...
  Includes a few thousand of the ASes
Stub ASes
  Do not provide transit service to others
  Connect to one or more upstream providers
  Includes vast majority (e.g., 85-90%) of the ASes

## Slide 37: Characteristics of the AS Graph
AS graph structure
  High variability in node degree (“power law”)
  A few very highly-connected ASes
  Many ASes have only a few connections
1
10
100
1000
CCDF
1
0.1
0.01
0.001
AS degree
All ASes have 1 or more neighbors
Very few have degree >= 100

## Slide 38: Characteristics of AS Paths
AS path may be longer than shortest AS path
Router path may be longer than shortest AS path
s
d
3 AS hops, 7 router hops
2 AS hops,
8 router hops

## Slide 39: Conclusions
Internet topology
  Network inside an AS
  Network connecting Ases